## Slide 1: FTC Software Intro (Robotc)
Team 5220 Roboknights

## Slide 2: Outline
Getting Started
  Hardware Setup/Wiring
  Software Setup/Pragmas
Programming with RobotC
  Grammar/Syntax
  Basic Statements
  Programming constructs, logic, etc.
  Style, organization
  Top 5 problems

## Slide 3: Wiring
Basic Setup:

## Slide 4: Software Setup
Pragmas – EXTREMELY IMPORTANT!
Connecting the robot by Bluetooth
  Turn on Bluetooth on computer and robot
  Add robot under “Bluetooth devices” on computer
  Go to “Communication Link Setup” in RobotC
  Select Robot and connect

## Slide 5: RobotC Syntax (“Grammar”)
The statement:
  Each statement tells the program to do something, e.g. move a motor.
  Statements can have parameters
  Statements are separated by semicolons.
  Lot of statements are pre-defined for you: if you think there should be a statement to do something, there probably is. Use google.
  Blocks, compound statements, curly brackets {}

## Slide 6: RobotC Syntax Continued
Tasks
  task main: This is what actually runs
  Creating new tasks
  Using your tasks: StartTask and StopTask
  Multithreading
Functions
  Similar syntax to tasks – Notable differences:
    Wait for completion
    Parameters
    Returning a value

## Slide 7: Variables
Variables are what we use to store data throughout the program.
  Declaration, e.g. int x;
  Assignment operator, =
  +=, ++, --
  Using variables
Most common variable types:
  Int: integer
  Double: decimal number
  String: string of characters, text segment
  Bool: boolean, true or false
Global vs. Local

## Slide 8: RobotC Basic Statements:
motor [motorName] = int power
  Sets a motor to a certain power, from – 100 to 100.
servo [servoName] = int position
  For a 180 degree servo, sets the servo position to the specified position, from 0 to 255.
  For a CR servo, if position < 127, moves backwards, if position > 127, moves forwards, if position == 127, stops.

## Slide 9: RobotC Basic Statements Continued:
SensorValue [sensorName]
  Reads the value of the specified sensor
nMotorEncoder [motorName]
  Reads the value of the specified motor encoder
wait1Msec (int time)
  Stops the program at this statement for the specified amount of time in milliseconds.

## Slide 10: RobotC Basic Statements Continued:
nxtDisplayTextLine (int lineNumber, string text)
And remember…
#define name value
  Assigns the value to the name for the rest of the gram, e.g. #define Number 72 means that “Number” can be used anywhere that 72 would.
#include filename.extension
  Adds the specified file as a header.

## Slide 11: Flow Control
Boolean testing, true or false
if, else if, and else system
switch, case, and default system
Loops
  while {} statement
  for () statement
Break, continue, and return: Escaping from the flow

## Slide 12: Compiling and Errors
Compiling: turns RobotC code into machine code.
Errors: The bane of all programming:
  Compiler
    The compiler helps point out errors, yet it can be misleading. Forgetting one bracket might lead to a boatload of errors in other places!
  Logical
    Not noticed by compiler, kind of like speaking correct grammar, but conveying the wrong meaning, e.g. variable x is 1 when it should be 2.

## Slide 13: Style and Organization
Standard Casing: Capital word-breaks for tasks, camel case for functions and variables
Name your variables sensibly!
Make code re-usable, e.g. code to move motors a certain distance belongs in a function
Add spacing, line breaks and indentation so you can read the code.
Store values used in multiple places in variables/constants that can easily be changed.
Comments: // and /*

## Slide 14: Typical Autonomous Program Format:

## Slide 15: Typical TeleOp Program Format:

## Slide 16: Top 5 annoying problems
Pragma Errors – especially when using encoders.
Locating logical errors – especially when logic in program is complex
Inconsistency of motor distances: Solve with encoders and sensors
Motors burning out: If nothing is moving, don’t try to move the motor more!
Messy / Hard to change code: Think of organization from the beginning.

## Slide 17: Contact Info
Website (with slides and example code):
www.theroboknights. com
Email:
theroboknights@gmail.com

## Slide 18: Thanks For Watching!
Any Questions?